Writing a Simulator for the SIMH System

Revised 1-Dec-01 for V2.8-0

1.	Overview	1

2.	Data Types	2

3.	VM Organization	2

3.1	CPU Organization	3

3.1.1	Time Base	4

3.1.2	Memory Organization	4

3.1.3	Interrupt Organization	4

3.1.4	I/O Dispatching	5

3.1.5	Instruction Execution	5

3.2	Peripheral Device Organization	6

3.2.1	Device Timing	7

3.2.2	Clock Calibration	8

3.2.3	Data I/O	9

4.	Data Structures	10

4.1	device Structure	10

4.1.1	Examine and Deposit Routines	11

4.1.2	Reset Routine	11

4.1.3	Boot Routine	11

4.1.4	Attach and Detach Routines	11

4.2	unit Structure	12

4.2.1	Unit Flags	13

4.2.2	Service Routine	13

4.3	reg Structure	13

4.3.1	Register Flags	15

4.4	mtab Structure	15

4.4.1	Validation Routine	17

4.4.2	Display Routine	17

4.5	Other Data Structures	17

5.	VM Provided Routines	18

5.1	Instruction Execution	18

5.2	Binary Load and Dump	18

5.3	Symbolic Examination and Deposit	18

5.4	Multi-Terminal Support (Telnet)	19

1.	Overview

SIMH (history simulators) is a set of portable programs, written in C, which simulate various historically interesting computers.  This document describes how to design, write, and check out a new simulator for SIMH.  It is not an introduction to either the philosophy or external operation of SIMH, and the reader should be familiar with both of those topics before proceeding.  Nor is it a guide to the internal design or operation of SIMH, except insofar as those areas interact with simulator design.  Instead, this manual presents and explains the form, meaning, and operation of the interfaces between simulators and the SIMH simulator control package.  It also offers some suggestions for utilizing the services SIMH offers and explains the constraints that all simulators operating within SIMH will experience.

Some terminology: Each simulator consists of a standard simulator control package (SCP), which provides a control framework and utility routines for a simulator; and a unique virtual machine (VM), which implements the simulated processor and selected peripherals.  A VM consists of multiple devices, such as the CPU, paper tape reader, disk controller, etc.  Each controller consists of a named state space (called registers) and one or more units.  Each unit consists of a numbered state space (called a data set).  The host computer is the system on which SIMH runs; the target computer is the system being simulated.

SIMH is unabashedly based on the MIMIC simulation system, designed in the late 1960’s by Len Fehskens, Mike McCarthy, and Bob Supnik.   This document is based on MIMIC’s published interface specification, “How to Write a Virtual Machine for the MIMIC Simulation System”, by Len Fehskens and Bob Supnik.

2.	Data Types

SIMH is written in C.  The host system must support (at least) 32-bit data types (64-bit data types for the PDP-10 and other large-word target systems).  To cope with the vagaries of C data types, SIMH defines some unambiguous data types for its interfaces:

SIMH data type			interpretation in typical 32-bit C

int8, uint8			char, unsigned char

int16, uint16			short, unsigned short

int32, uint32			int, unsigned int

t_int64, t_uint64			long long, _int64 (system specific)

t_addr				simulated address, int32

t_value				simulated value, unsigned int32 or int64

t_svalue			simulated signed value, int32 or int64

t_mtrec				mag tape record length, int32

t_stat				status code, int

t_bool				true/false value, int

[The inconsistency in naming t_int64 and t_uint64 is due to VC++, which uses int64 as a structure name member in the master Windows definitions file.]

In addition, SIMH defines structures for each of its major data elements

DEVICE			device definition structure

UNIT				unit definition structure

REG				register definition structure

MTAB				modifier definition structure

3.	VM Organization

A virtual machine (VM) is a collection of devices bound together through their internal logic.  Each device is named and corresponds more or less to a hunk of hardware on the real machine; for example:

VM device			Real machine hardware

CPU				central processor and main memory

PTR				paper tape reader controller and paper tape reader

TTI				console keyboard

TTO				console output

DKP				disk pack controller and drives

There may be more than one device per physical hardware entity, as for the console; but for each user-accessible device there must be at least one.  One of these devices will have the pre-eminent responsibility for directing simulated operations.  Normally, this is the CPU, but it could be a higher-level entity, such as a bus master.

The VM actually runs as a subroutine of the simulator control package (SCP).  It provides a master routine for running simulated programs and other routines and data structures to implement SCP’s command and control functions.  The interfaces between a VM and SCP are relatively few:

Interface			Function

char sim_name[]		simulator name string

REG *sim_pc			pointer to simulated program counter

int32 sim_emax		maximum number of words in an instruction

DEVICE *sim_devices[]	table of pointers to simulated devices, NULL terminated

UNIT *sim_consoles[]		table of pointers to simulated consoles

char *sim_stop_messages[]	table of pointers to error messages

t_stat sim_load (…)		binary loader subroutine

t_stat sim_inst (void)		instruction execution subroutine

t_stat parse_sym (…)		symbolic instruction parse subroutine (optional)

t_stat fprint_sym (…)		symbolic instruction print subroutine (optional)

There is no required organization for VM code.  The following convention has been used so far.  Let name be the name of the real system (i1401 for the IBM 1401; pdp1 for the PDP-1; pdp18b for the other 18-bit PDP’s; pdp8 for the PDP-8; pdp11 for the PDP-11; nova for Nova; hp2100 for the HP 21XX; id4 for the Interdata 4; pdp10 for the PDP-10):

·	name.h contains definitions for the particular simulator

·	name_sys.c contains all the SCP interfaces except the instruction simulator

·	name_cpu.c contains the instruction simulator and CPU data structures

·	name_stddev.c contains the peripherals which were standard with the real system.

·	name_lp.c contains the line printer.

·	name_mt.c contains the mag tape controller and drives, etc.

The SIMH standard definitions are in sim_defs.h, the simulator control package in scp.c, and the operating-system dependent terminal routines in scp_tty.c.  Additional libraries include sim_tmxr.c (header file sim_tmxr.h) for terminal multiplexors, and sim_sock.c (header file sim_sock.h) for network processing.

3.1	CPU Organization

Most CPU’s perform at least the following functions:

·	Time keeping

·	Instruction fetching

·	Address decoding

·	Execution of non-I/O instructions

·	I/O command processing

·	Interrupt processing

Instruction execution is actually the least complicated part of the design; memory and I/O organization should be tackled first.

3.1.1	Time Base

In order to simulate asynchronous events, such as I/O completion, the VM must define and keep a time base.  This can be accurate (for example, nanoseconds of execution) or arbitrary (for example, number of instructions executed), but it must be consistently used throughout the VM.  All existing VM’s count time in instructions.

The CPU is responsible for counting down the event counter sim_interval and calling the asynchronous event controller sim_process_event.  The record keeping for timing is done by SCP.

3.1.2	Memory Organization

The criterion for memory layout is very simple: use the SIMH data type that is as large as (or if necessary, larger than), the word length of the real machine.  Note that the criterion is word length, not addressability: the PDP-11 has byte addressable memory, but it is a 16-bit machine, and its memory is defined as uint16 M[].  It may seem tempting to define memory as a union of int8 and int16 data types, but this would make the resulting VM endian-dependent.  Instead, the VM should be based on the underlying word size of the real machine, and byte manipulation should be done explicitly.  Examples:

Simulator		memory size		memory declaration

IBM 1401		6-bit			uint8

PDP-8			12-bit			uint16

PDP-11, Nova		16-bit			uint16

PDP-1			18-bit			uint32

PDP-10			36-bit			uint64

3.1.3	Interrupt Organization

The design of the VM’s interrupt structure is a complex interaction between efficiency and fidelity to the hardware.  If the VM’s interrupt structure is too abstract, interrupt driven software may not run.  On the other hand, if it follows the hardware too literally, it may significantly reduce simulation speed.  One rule I can offer is to minimize the fetch-phase cost of interrupts, even if this complicates the (much less frequent) evaluation of the interrupt system following an I/O operation or asynchronous event.  Another is not to over-generalize; even if the real hardware could support 64 or 256 interrupting devices, the simulators will be running much smaller configurations.  I’ll start with a simple interrupt structure and then offer suggestions for generalization.

In the simplest structure, interrupt requests correspond to device flags and are kept in an interrupt request variable, with one flag per bit.  The fetch-phase evaluation of interrupts consists of two steps: are interrupts enabled, and is there an interrupt outstanding?  If all the interrupt requests are kept as single-bit flags in a variable, the fetch-phase test is very fast:

if (int_enable && int_requests) { …process interrupt… }

Indeed, the interrupt enable flag can be made the highest bit in the interrupt request variable, and the two tests combined:

if (int_requests > INT_ENABLE) { …process interrupt… }

Setting or clearing device flags directly sets or clears the appropriate interrupt request flag:

set: 	int_requests = int_requests | DEVICE_FLAG;

clear:	int_requests = int_requests & ~DEVICE_FLAG;

At a slightly higher complexity, interrupt requests do not correspond directly to device flags but are based on masking the device flags with an enable (or disable) mask.  There are now three parallel variables: interrupt requests, device flags, and interrupt enable mask.  The fetch-phase test does not change; however, the evaluation of whether an interrupt is pending now requires an extra step:

enable:	int_requests = device_flags & int_enables;

disable:	int_requests = device_flags & ~int_disables;

If required for interrupt processing, the highest priority interrupting device can be determined by scanning the interrupt request variable from high priority to low until a set bit is found.  The bit position can then be back-mapped through a table to determine the address or interrupt vector of the interrupting device.

At yet higher complexity, the interrupt system may be too complex or too large to evaluate during the fetch-phase.  In this case, an interrupt pending flag is created, and it is evaluated by subroutine call whenever a change could occur (start of execution, I/O instruction issued, device time out occurs).  This makes fetch-phase evaluation simple and isolates interrupt evaluation to a common subroutine.

3.1.4	I/O Dispatching

I/O dispatching consists of four steps:

·	Identify the I/O command and analyze for the device address.

·	Locate the selected device.

·	Break down the I/O command into standard fields.

·	Call the device processor.

Analyzing an I/O command is usually easy.  Most systems have one or more explicit I/O instructions containing an I/O command and a device address.  Memory mapped I/O is more complicated; the identification of a reference to I/O space becomes part of memory addressing.  This usually requires centralizing memory reads and writes into subroutines, rather than as inline code.

Once an I/O command has been analyzed, the CPU must locate the device subroutine.  The simplest way is a large switch statement with hardwired subroutine calls.  Slightly more modular is to call through a dispatch table, with NULL entries representing non-existent devices.  Before calling the device routine, the CPU usually breaks down the I/O command into standard fields.  This simplifies writing the peripheral simulator.

3.1.5	Instruction Execution

Instruction execution is the responsibility of VM subroutine sim_instr.  It is called from SCP as a result of a RUN, GO, CONT, or BOOT command.  It begins executing instructions at the current PC (sim_PC points to its register description block) and continues until halted by an error or an external event.

When called, the CPU needs to account for any state changes that the user made.  For example, it may need to re-evaluate whether an interrupt is pending, or restore frequently used state to local register variables for efficiency.  The actual instruction fetch and execute cycle is usually structured as a loop controlled by an error variable, e.g.,

reason = 0;

do { … } while (reason == 0);	or	while (reason == 0) { … }

Within this loop, the usual order of events is:

·	If the event timer sim_interval has reached zero, process any timed events.  This is done by SCP subroutine sim_process_event.  Because this is the polling mechanism for user-generated processor halts (^E), errors must be recognized immediately:

if (sim_interval <= 0) {

if (reason = sim_process_event ()) break;  }

·	Check for outstanding interrupts and process if required.

·	Check for other processor-unique events, such as wait-state outstanding or traps outstanding.

·	Check for an instruction breakpoint.  SCP has no breakpoint facility, but it is customary to implement a single instruction breakpoint to help with processor code.  All the existing CPU’s use the same mechanism, see the sources for details.

·	Fetch the next instruction, increment the PC, optionally decode the address, and dispatch (via a switch statement) for execution.

A few guidelines for implementation:

·	In general, code should reflect the hardware being simulated.  This is usually simplest and easiest to debug.

·	The VM should provide some debugging aids.  The existing CPU’s all provide an instruction breakpoint, an OLDPC register, and error stops on invalid instructions or operations.

3.2	Peripheral Device Organization

The basic elements of a VM are devices, each corresponding roughly to a real chunk of hardware.  A device consists of register-based state and one or more units.  Thus, a multi-drive disk subsystem is a single device (representing the hardware of the real controller) and one or more units (each representing a single disk drive).  Sometimes the device and its unit are the same entity as, for example, in the case of a paper tape reader.  However, a single physical device, such as the console, may be broken up for convenience into separate input and output devices.

In general, units correspond to individual sources of input or output (one tape transport, one A-to-D channel).  Units are the basic medium for both device timing and device I/O.  Except for the console, all I/O devices are simulated as host-resident files.  SCP allows the user to make an explicit association between a host-resident file and a simulated hardware entity.

Both devices and units have state.  Devices operate on registers, which contain information about the state of the device, and indirectly, about the state of the units.  Units operate on data sets, which may be thought of as individual instances of input or output, such as a disk pack or a punched paper tape.  In a typical multi-unit device, all units are the same, and the device performs similar operations on all of them, depending on which one has been selected by the program being simulated.

(Note: SIMH, like MIMIC, restricts registers to devices. Replicated registers, for example, disk drive current state, are handled via register arrays.)

For each structural level, SIMH defines, and the VM must supply, a corresponding data structure.  device structures correspond to devices, reg structures to registers, and unit structures to units.  These structures are described in detail in section 4.

The primary functions of a peripheral are:

·	command decoding and execution

·	device timing

·	data transmission.

Command decoding is fairly obvious.  At least one section of the peripheral code module will be devoted to processing directives issued by the CPU.  Typically, the command decoder will be responsible for register and flag manipulation, and for issuing or canceling I/O requests.  The former is easy, but the later requires a thorough understanding of device timing.

3.2.1	Device Timing

The principal problem in I/O device simulation is imitating asynchronous operations in a sequential simulation environment.  Fortunately, the timing characteristics of most I/O devices do not vary with external circumstances.  The distinction between devices whose timing is externally generated (e.g., console keyboard) and those whose timing is externally generated (disk, paper tape reader) is crucial.  With an externally timed device, there is no way to know when an in-progress operation will begin or end; with an internally timed device, given the time when an operation starts, the end time can be calculated.

For an internally timed device, the elapsed time between the start and conclusion of an operation is called the wait time.  Some typical internally timed devices and their wait times include:

PTR (300 char/sec)		3.3 msec

PTP (50 char/sec)		20 msec

CLK (line frequency)		16.6 msec

TTO (30 char/sec)		33 msec

Mass storage devices, such as disks and tapes, do not have a fixed response time, but a start-to-finish time can be calculated based on current versus desired position, state of motion, etc.

For an externally timed device, there is no portable mechanism by which a VM can be notified of an external event.  Because the only important externally timed device is the console keyboard, all current VM’s poll for keyboard input, thus converting the externally timed keyboard to a pseudo-internally timed device.

SCP provides the supporting routines for device timing.  SCP maintains a list of devices (called active devices) which are in the process of timing out.  It also provides routines for querying or manipulating this list (called the active queue).  Lastly, it provides a routine for checking for timed-out units and executing a VM-specified action when a time-out occurs.

Device timing is done with the UNIT structure, described in section 3.  To set up a timed operation, the peripheral calculates a waiting period for a unit and places that unit on the active queue.  The CPU counts down the waiting period.  When the waiting period has expired, sim_process_event removes the unit from the active queue and calls a device subroutine.  A device may also cancel an outstanding timed operation and query the state of the queue.  The timing subroutines are:

·	t_stat sim_activate (UNIT *uptr, int32 wait).  This routine places the specified unit on the active queue with the specified waiting period.  A waiting period of 0 is legal; negative waits cause an error.  If the unit is already active, the active queue is not changed, and no error occurs.

·	t_stat sim_cancel (UNIT *uptr).  This routine removes the specified unit from the active queue.  If the unit is not on the queue, no error occurs.

·	int32 sim_is_active (UNIT *uptr).  This routine tests whether a unit is in the active queue.  If it is, the routine returns the time (+1) remaining; if it is not, the routine returns 0.

·	double sim_gtime (void).  This routine returns the time elapsed since the last RUN or BOOT command.

·	uint32 sim_grtime (void).  This routine returns the low-order 32b of the time elapsed since the last RUN or BOOT command.

·	int32 sim_qcount (void).  This routine returns the number of entries on the clock queue.

·	t_stat sim_process_event (void).  This routine removes all timed out units from the active queue and calls the appropriate device subroutine to service the time-out.

·	int32 sim_interval.  This variable counts down the first outstanding timed event.  If there are no timed events outstanding, SCP counts down a “null interval” of 10,000 time units.

3.2.2	Clock Calibration

The timing mechanism described in the previous section is approximate.  Devices, such as real-time clocks, which track wall time will be inaccurate.  SCP provides routines to synchronize a simulated real-time clock to wall time.

·	int32 sim_rtc_init (int32 clock_interval).  This routine initializes the clock calibration mechanism.  The argument is returned as the result.

·	int32 sim_rtc_calb (int32 tickspersecond).  This routine calibrates the real-time clock.  The argument is the number of clock ticks expected per second.

The simulator calls sim_rtc_init in the prolog of sim_instr, before instruction execution starts, and whenever the real-time clock is started.  The simulator calls sim_rtc_calb to calculate the actual interval delay when the real-time clock is serviced:

/* clock start */

if (!sim_is_active (&clk_unit)) sim_activate (&clk_unit, sim_rtc_init (clk_delay));

etc.

/* clock service */

sim_activate (&clk_unit, sim_rtc_calb (clk_ticks_per_second);

3.2.3	Data I/O

For most devices, timing is half the battle (for clocks it is the entire war); the other half is I/O.  Except for the console, all I/O devices are simulated as files on the host file system in little-endian format.  SCP provides facilities for associating files with units (ATTACH command) and for reading and writing data from and to devices in a endian- and size-independent way.

For most devices, the VM designer does not have to be concerned about the formatting of simulated device files.  I/O occurs in 1, 2, or 4 byte quantities; SCP automatically chooses the correct data size and corrects for byte ordering.  Specific issues:

·	Line printers should write data as 7-bit ASCII, with newlines replacing carriage-return/line-feed sequences.

·	Disks should be viewed as linear data sets, from sector 0 of surface 0 of cylinder 0 to the last sector on the disk.  This allows easy transcription of real disks to files usable by the simulator.

·	Magtapes, by convention, use a record based format.  Each record consists of a leading 32-bit record length, the record data (padded with a byte of 0 if the record length is odd), and a trailing 32-bit record length.  File marks are recorded as one record length of 0.

·	Cards have 12 bits of data per column, but the data is most conveniently viewed as (ASCII) characters.  Existing card reader simulators do not support binary operation.

Data I/O varies between fixed and variable capacity devices, and between buffered and non-buffered devices.  A fixed capacity device differs from a variable capacity device in that the file attached to the former has a maximum size, while the file attached to the latter may expand indefinitely.  A buffered device differs from a non-buffered device in that the former buffers its data set in host memory, while the latter maintains it as a file.  Most variable capacity devices (such as the paper tape reader and punch) are sequential; all buffered devices are fixed capacity.

3.2.3.1	Reading and Writing Data

The ATTACH command creates an association between a host file and an I/O unit.  For non-buffered devices, ATTACH stores the file pointer for the host file in the fileref field of the UNIT structure.  For buffered devices, ATTACH reads the entire host file into an allocated buffer pointed to by the filebuf field of the UNIT structure.

For non-buffered devices, I/O is done with standard C subroutines plus the SCP routines fxread and fxwrite.  fxread and fxwrite are identical in calling sequence and function to fread and fwrite, respectively, but will correct for endian dependencies.  For buffered devices, I/O is done by copying data to or from the allocated buffer.  The device code must maintain the number (+1) of the highest address modified in the hwmark field of the UNIT structure.  For both the non-buffered and buffered cases, the device must perform all address calculations and positioning operations.

The DETACH command breaks the association between a host file and an I/O unit.  For buffered devices, DETACH writes the allocated buffer back to the host file.

3.2.3.2	Console I/O

SCP provides two routines for console I/O.

·	t_stat sim_poll_char (void).  This routine polls for keyboard input.  If there is a character, it returns SCPE_KFLAG + the character.  If the user typed the interrupt character (^E), it returns SCPE_STOP.  If there is no input, it returns SCPE_OK.

·	t_stat sim_putchar (int32 char).  This routine types the specified ASCII character on the console.  There are no errors.

4.	Data Structures

The devices, units, and registers which make up a VM are formally described through a set of data structures which interface the VM to the control portions of SCP.  The devices themselves are pointed to by the device list array sim_devices[].  Within a device, both units and registers are allocated contiguously as arrays of structures.  In addition, many devices allow the user to set or clear options via a modifications table.

4.1	device Structure

Devices are defined by the device structure (typedef DEVICE):

struct device {

char		*name;				/* name */

struct unit 	*units;				/* units */

struct reg	*registers;			/* registers */

struct mtab	*modifiers;			/* modifiers */

int		numunits;			/* #units */

int		aradix;				/* address radix */

int		awidth;				/* address width */

int		aincr;				/* addr increment */

int		dradix;				/* data radix */

int		dwidth;				/* data width */

t_stat		(*examine)();			/* examine routine */

t_stat		(*deposit)();			/* deposit routine */

t_stat		(*reset)();			/* reset routine */

t_stat		(*boot)();			/* boot routine */

t_stat		(*attach)();			/* attach routine */

t_stat		(*detach)();			/* detach routine */

};

The fields are the following:

name		device name, string of all capital alphanumeric characters.

units		pointer to array of unit structures, or NULL if none.

registers	pointer to array of reg structures, or NULL if none.

modifiers	pointer to array of mtab structures, or NULL if none.

numunits 	number of units in this device.

aradix		radix for input and display of device addresses, 2 to 16 inclusive.

awidth		width in bits of a device address, 1 to 31 inclusive.

aincr	increment between device addresses, normally 1; however, byte addressed devices with 16-bit words specify 2, with 32-bit words 4.

dradix		radix for input and display of device data, 2 to 16 inclusive.

dwidth		width in bits of device data, 1 to 32 inclusive.

examine	address of special device data read routine, or NULL if none is required.

deposit		address of special device data write routine, or NULL if none is required.

reset		address of device reset routine, or NULL if none is required.

boot		address of device bootstrap routine, or NULL if none is required.

attach		address of special device attach routine, or NULL if none is required.

detach		address of special device detach routine, or NULL if none is required.

4.1.1	Examine and Deposit Routines

For devices which maintain their data sets as host files, SCP implements the examine and deposit data functions.  However, devices which maintain their data sets as private state (typically just the CPU) must supply special examine and deposit routines.  The calling sequences are:

t_stat examine_routine (t_val *eval_array, t_addr addr, UNIT *uptr, int32 switches) – Copy sim_emax consecutive addresses for unit uptr, starting at addr, into eval_array.  The switch variable has bit<n> set if the n’th letter was specified as a switch to the examine command.

t_stat deposit_routine (t_val value, t_addr addr, UNIT *uptr, int32 switches) – Store the specified value in the specified addr for unit uptr.  The switch variable is the same as for the examine routine.

4.1.2	Reset Routine

The reset routine implements the device reset function for the RESET, RUN, and BOOT commands.  Its calling sequence is:

t_stat reset_routine (DEVICE *dptr) – Reset the specified device to its initial state.

A typical reset routine clears all device flags and cancels any outstanding timing operations.

4.1.3	Boot Routine

If a device responds to a BOOT command, the boot routine implements the bootstrapping function.  Its calling sequence is:

t_stat boot_routine (int32 unit_number) – Bootstrap the specified unit.

A typical bootstrap routine copies a bootstrap loader into main memory and sets the PC to the starting address of the loader.  SCP then starts simulation at the specified address.

4.1.4	Attach and Detach Routines

Normally, the ATTACH and DETACH commands are handled by SCP.  However, devices which need to pre- or post-process these commands must supply special attach and detach routines.  The calling sequences are:

t_stat attach_routine (UNIT *uptr, char *file) – Attach the specified file to the unit uptr.

t_stat detach_routine (UNIT *uptr) – Detach unit uptr.

In practice, these routines always invoke the standard SCP routines, attach_unit and detach_unit, respectively.  For example, here are special attach and detach routines to update line printer error state:

t_stat lpt_attach (UNIT *uptr, char *cptr) {

t_stat r;

if ((r = attach_unit (uptr, cptr)) != SCPE_OK) return r;

lpt_error = 0;

return SCPE_OK;

}

t_stat lpt_detach (UNIT *uptr) {

lpt_error = 1;

return detach_unit (uptr);

}

SCP executes a DETACH ALL command as part of simulator exit.  Normally, DETACH ALL only calls a unit’s detach routine if the unit’s UNIT_ATTABLE flag is set.  During simulator exit, the detach routine is called unconditionally.  This allows the detach routine of a non-attachable unit to function as a simulator-specific cleanup routine for the unit, device, or entire simulator.

4.2	unit Structure

Units are allocated as contiguous array.  Each unit is defined with a unit structure (typedef UNIT):

struct unit {

struct unit	*next;				/* next active */

t_stat		(*action)();			/* action routine */

char		*filename;			/* open file name */

FILE		*fileref;				/* file reference */

void		*filebuf;				/* memory buffer */

t_addr		hwmark;			/* high water mark */

int32		time;				/* time out */

int32		flags;				/* flags */

t_addr		capac;				/* capacity */

t_addr		pos;				/* file position */

int32		buf;				/* buffer */

int32		wait;				/* wait */

int32		u3;				/* device specific */

int32		u4;				/* device specific */

};

The fields are the following:

next		pointer to next unit in active queue, NULL if none.

action		address of unit time-out service routine.

filename	pointer to name of attached file, NULL if none.

fileref		pointer to FILE structure of attached file, NULL if none.

hwmark	buffered devices only; highest modified address, + 1.

time		increment until time-out beyond previous unit in active queue.

flags		unit flags.

capac		unit capacity, 0 if variable.

pos		sequential devices only; next device address to be read or written.

buf		by convention, the unit buffer, but can be used for other purposes.

wait		by convention, the unit wait time, but can be used for other purposes.

u3		user-defined.

u4		user-defined.

buf, wait, u3, u4 are all saved and restored by the SAVE and RESTORE commands and thus can be used for unit state which must be preserved.

Macro UDATA is available to fill in the common fields of a UNIT.  It is invoked by

UDATA		(action_routine, flags, capacity)

Fields after buf can be filled in manually, e.g,

UNIT lpt_unit = { UDATA (&lpt_svc, UNIT_SEQ+UNIT_ATTABLE, 0), 500 };

defines the line printer as a sequential unit with a wait time of 500.

4.2.1	Unit Flags

The flags field contains indicators of current unit status.  SIMH defines 11 flags:

flag name		meaning if set

UNIT_DISABLE		the unit responds to ENABLE and DISABLE.

UNIT_DIS		the unit is currently disabled.

UNIT_ATTABLE	the unit responds to ATTACH and DETACH.

UNIT_ATT		the unit is currently attached to a file.

UNIT_BUFABLE	the unit can buffer its data set in memory.

UNIT_MUSTBUF	the unit must buffer its data set in memory.

UNIT_BUF		the unit is currently buffering its data set in memory.

UNIT_ROABLE		the unit can be ATTACHed read only.

UNIT_RO		the unit is currently read only.

UNIT_SEQ		the unit is sequential.

UNIX_FIX		the unit is fixed capacity.

UNIT_BINK		the unit measures “K” as 1024, rather than 1000.

Starting at bit position UNIT_V_UF, the remaining flags are device-specific.  Device-specific flags are set and cleared with the SET and CLEAR commands, which reference the MTAB array (see below).  Device-specific flags and UNIT_DIS are not automatically saved and restored; the device must supply a register covering these bits.

4.2.2	Service Routine

This routine is called by sim_process_event when a unit times out.  Its calling sequence is:

t_stat service_routine (UNIT *uptr)

The status returned by the service routine is passed by sim_process_event back to the CPU.

4.3	reg Structure

Registers are allocated as contiguous array, with a NULL register at the end.  Each register is defined with a reg structure (typedef REG):

struct reg {

char		*name;				/* name */

void		*loc;				/* location */

int		radix;				/* radix */

int		width;				/* width */

int		offset;				/* starting bit */

int		depth;				/* save depth */

int32		flags;				/* flags */

};

The fields are the following:

name		device name, string of all capital alphanumeric characters.

loc		pointer to location of the register value.

radix		radix for input and display of data, 2 to 16 inclusive.

width		width in bits of data, 1 to 32 inclusive.

width		bit offset (from right end of data).

depth		size of data array (normally 1).

flags		flags and formatting information.

The depth field is used with “arrayed registers”.  Arrayed registers are used to represent structures with multiple data values, such as the locations in a transfer buffer; or structures which are replicated in every unit, such as a drive status register.

Macros ORDATA, DRDATA, and HRDATA define right-justified octal, decimal, and hexidecimal registers, respectively.  They are invoked by:

xRDATA	(name, location, width)

Macro FLDATA defines a one-bit binary flag at an arbitrary offset in a 32-bit word.  It is invoked by:

FLDATA	(name, location, bit_position)

Macro GRDATA defines a register with arbitrary location and radix.  It is invoked by:

GRDATA	(name, location, radix, width, bit_position)

Macro BRDATA defines an arrayed register whose data is kept in a standard C array.  It is invoked by:

BRDATA	(name, location, radix, width, depth)

For all of these macros, the flag field can be filled in manually, e.g.,

REG lpt_reg = {

{ DRDATA	(POS, lpt_unit.pos, 31), PV_LFT }, … }

Finally, macro URDATA defines an arrayed register whose data is part of the UNIT structure.  This macro must be used with great care.  If the fields are set up wrong, or the data is actually kept somewhere else, storing through this register declaration can trample over memory.  The macro is invoked by:

URDATA	(name, location, radix, width, offset, depth, flags)

The location should be an offset in the UNIT structure for unit 0.  The flags can be any of the normal register flags; REG_UNIT will be OR’d in automatically.  For example, the following declares an arrayed registers of all the UNIT position fields in a device with 4 units:

{ URDATA	(POS, dev_unit[0].pos, 8, 31, 0, 4, 0) }

4.3.1	Register Flags

The flags field contains indicators that control register examination and deposit.

flag name		meaning if specified

PV_RZRO		print register right justified with leading zeroes.

PV_RSPC		print register right justified with leading spaces.

PV_LEFT		print register left justified.

REG_RO		register is read only.

REG_HIDDEN		register is hidden (will not appear in EXAMINE STATE).

REG_HRO		register is read only and hidden.

REG_NZ		new register values must be non-zero.

REG_UNIT		register resides in the UNIT structure.

4.4	mtab Structure

Device-specific SHOW and SET commands are processed using the modifications array, which is allocated as contiguous array, with a NULL at the end.  Each possible modification is defined with a mtab structure (synonym MTAB), which has the following fields:

struct mtab {

int32		mask;				/* mask */

int32		match;				/* match */

char		*pstring;			/* print string */

char		*mstring;			/* match string */

t_stat		(*valid)();			/* validation routine */

t_stat		(*disp)();			/* display routine */

void		*desc;				/* location descriptor */

};

MTAB supports two different structure interpretations: regular and extended.  A regular MTAB entry modifies flags in the UNIT flags word; the descriptor entry is not used.  The fields are the following:

mask		bit mask for testing the unit.flags field

match	value to be stored (SET) or compared (SHOW)

pstring	pointer to character string printed on a match (SHOW), or NULL

mstring	pointer to character string to be matched (SET), or NULL

valid	address of validation routine (SET), or NULL

disp	address of display routine (SHOW), or NULL

For SET, a regular MTAB entry is interpreted as follows:

1.	Test to see if the mstring entry exists.

2.	Test to see if the SET parameter matches the mstring.

3.	Call the validation routine, if any.

4.	Apply the mask value to the UNIT flags word and then or in the match value.

For SHOW, a regular MTAB entry is interpreted as follows:

1.	Test to see if the pstring entry exists.

2.	Test to see if the UNIT flags word, masked with the mask value, equals the match value.

3.	If a display routine exists, call it, otherwise

4.	Print the pstring.

Extended MTAB entries have a different interpretation:

mask		entry flags

MTAB_XTD	extended entry

MTAB_VDV	valid for devices

MTAB_VUN	valid for units

MTAB_VAL	takes a value

MTAB_NMO	valid only in named SHOW

match	value to be stored (SET)

pstring	pointer to character string printed on a match (SHOW), or NULL

mstring	pointer to character string to be matched (SET), or NULL

valid	address of validation routine (SET), or NULL

disp	address of display routine (SHOW), or NULL

desc	pointer to a REG structure (MTAB_VAL set) or

an int32 (MTAB_VAL clear)

For SET, an extended MTAB entry is interpreted as follows:

1.	Test to see if the mstring entry exists.

2.	Test to see if the SET parameter matches the mstring.

3.	Test to see if the entry is valid for the type of SET being done (SET device or SET unit).

4.	If a validation routine exists, call it and return its status.

5.	If desc is NULL, exit; validation routine presumably stored result.

6.	If MTAB_VAL is set, parse the SET option for “option=n”, and store the value n in the register described by desc.

7.	Otherwise, store the match value in the int32 pointed to by desc.

For SHOW, an extended MTAB entry is interpreted as follows:

1.	Test to see if the pstring entry exists.

2.	Test to see if the entry is valid for the type of SHOW being done (device or unit).

3.	If a display routine exists, call it, otherwise,

4.	If MTAB_VAL is set, print “=n”, where the value, radix, and width are taken from the register described by desc, otherwise,

5.	Print the pstring.

SHOW {dev|unit} <modifier> is a special case.  Only two kinds of modifiers can be displayed individually: an extended MTAB entry that takes a value; and any MTAB entry with both a display routine and a pstring.  Recall that if a display routine exists, SHOW does not use the pstring entry.  For displaying a named modifier, pstring is used as the string match.  This allows implementation of complex display routines that are only invoked by name, e.g.,

MTAB cpu_tab[] = {

{ mask, value, “normal”, “NORMAL”, NULL, NULL, NULL },

{ MTAB_XTD|MTAB_VDV|MTAB_NMO, 0, “SPECIAL”,

NULL, NULL, NULL, &spec_disp },

{ 0 } };

A SHOW CPU command will display only the modifier named NORMAL; but SHOW CPU SPECIAL will invoke the special display routine.

4.4.1	Validation Routine

The validation routine can be used to validate input during SET processing.  It can make other state changes required by the modification or initiate additional dialogs needed by the modifier.  Its calling sequence is:

t_stat validation_routine (UNIT *uptr, int32 value, char *cptr, void *desc) – test that uptr.flags can be set to value.  cptr points to the value portion of the parameter string (any characters after the = sign); if cptr is NULL, no value was given.  desc points to the REG or int32 used to store the parameter.

4.4.2	Display Routine

The display routine is called during SHOW processing to display device- or unit-specific state.  Its calling sequence is:

t_stat display_routine (FILE *st, UNIT *uptr, void *desc) – output device- or unit-specific state for uptr to stream st. desc points to the REG or int32 used to store the parameter.

When the display routine is called for a regular MTAB entry, SHOW has output the pstring argument but has not appended a newline.  When it is called for an extended MTAB entry, SHOW hasn’t output anything.  SHOW will append a newline after the display routine returns.

4.5	Other Data Structures

char sim_name[] is a character array containing the VM name.

int32 sim_emax contains the maximum number of words needed to hold the largest instruction or data item in the VM.  Examine and deposit will process up to sim_emax words.

DEVICE *sim_devices[] is an array of pointers to all the devices in the VM.  It is terminated by a NULL.  By convention, the CPU is always the first device in the array.

UNIT *sim_consoles[] is an array of pointers to the units of simulated consoles, alternating input and output.  (If a console has only an input unit, the output slot should also point to the input unit.)  This structure is only used for multi-console support.  If the VM has only one console, the pointer should be NULL.

REG *sim_PC points to the reg structure for the program counter.  By convention, the PC is always the first register in the CPU’s register array.

char *sim_stop_messages[] is an array of pointers to character strings, corresponding to error status returns greater than zero.  If sim_instr returns status code n > 0, then sim_stop_message[n] is printed by SCP.

5.	VM Provided Routines

5.1	Instruction Execution

Instruction execution is performed by routine sim_instr.  Its calling sequence is:

t_stat sim_instr (void) – Execute from current PC until error or halt.

5.2	Binary Load and Dump

If the VM responds to the LOAD (or DUMP) command, the loader (dumper) is implemented by routine sim_load.  Its calling sequence is:

t_stat sim_load (FILE *fptr, char *buf, char *fnam, t_bool flag) - If flag = 0, load data from binary file fptr.  If flag = 1, dump data to binary file fptr.  For either command, buf contains any VM-specific arguments, and fnam contains the file name.

If LOAD or DUMP is not implemented, sim_load should simply return SCPE_ARG.  The LOAD and DUMP commands open and close the specified file for sim_load.

5.3	Symbolic Examination and Deposit

If the VM provides symbolic examination and deposit of data, it must provide two routines, fprint_sym for output and parse_sym for input.  Their calling sequences are:

t_stat fprint_sym (FILE *ofile, t_addr addr, t_value *val, UNIT *uptr, int32 switch) – Based on the switch variable, symbolically output to stream ofile the data in array val at the specified addr in unit uptr.

t_stat parse_sym (char *cptr, t_addr addr, UNIT *uptr, t_value *val, int32 switch) – Based on the switch variable, parse character string cptr for a symbolic value val at the specified addr in unit uptr.

If symbolic processing is not implemented, or the output value or input string cannot be parsed, these routines should return SCPE_ARG.  If the processing was successful and consumed more than a single word, then these routines should return extra number of words (not bytes) consumed as a negative number.  If the processing was successful and consumed a single word, then these routines should return SCPE_OK.  For example, PDP-11 parse_sym would respond as follows to various inputs:

input				return value

XYZGH				SCPE_ARG

MOV R0,R1			SCPE_OK

MOV #4,R5			-1

MOV 1234,5670		-2

The interpretation of switch values is arbitrary, but the following are used by existing VM’s:

switch				interpretation

-a				single character

-c				character string

-m				instruction mnemonic

In addition, on input, a leading ‘ (apostrophe) is interpreted to mean a single character, and a leading “ (double quote) is interpreted to mean a character string.

5.4	Multi-Terminal Support (Telnet)

SIMH supports the use of multiple terminals.  All terminals except the console are accessed via Telnet.  SIMH provides two supporting libraries for implementing multiple terminals: sim_tmxr.c (and its header file, sim_tmxr.h), which provide OS-independent support routines for terminal multiplexors; and sim_sock.c (and its header file, sim_sock.h), which provide OS-dependent socket routines.  Sim_sock.c is presently implemented only under Windows and UNIX.

Two basic data structures define the multiple terminals.  Individual lines are defined by the tmln structure (typedef TMLN):

struct tmln {

SOCKET	conn;				/* line conn */

uint32		ipad;				/* IP address */

uint32		cnms;				/* connect  time ms */

int32		tsta;				/* Telnet state */

int32		rcve;				/* rcv enable */

int32		xmte;				/* xmt enable */

int32		dstb;				/* disable Tlnt bin */

int32		rxbpr;				/* rcv buf remove */

int32		rxbpi;				/* rcv buf insert */

int32		rxcnt;				/* rcv count */

int32		txbpr;				/* xmt buf remove */

int32		txbpi;				/* xmt buf insert */

int32		txcnt;				/* xmt count */

uint8		rxb[TMXR_MAXBUF];		/* rcv buffer */

uint8		txb[TMXR_MAXBUF];		/* xmt buffer */

};

The fields are the following:

conn		connection socket (0 = disconnected)

tsta		Telnet state

rcve		receive enable flag (0 = disabled)

xmte		transmit flow control flag (0 = transmit disabled)

dstb		Telnet bin mode disabled

rxbpr		receive buffer remove pointer

rxbpi		receive buffer insert pointer

rxcnt		receive count

txbpr		transmit buffer remove pointer

txbpi		transmit buffer insert pointer

txcnt		transmit count

rxb		receive buffer

txb		transmit buffer

The overall set of extra terminals is defined by the tmxr structure (typedef TMXR):

struct tmxr {

int32		lines;				/* # lines */

SOCKET	master;				/* master socket */

TMLN		*ldsc[TMXR_MAXLIN];		/* line descriptors */

};

The fields are the following:

lines		number of lines (constant)

master		master listening socket (specified by ATTACH command)

ldsc		array of line descriptors

Library sim_tmxr.c provides the following routines to support Telnet-based terminals:

int32 tmxr_poll_conn (TMXR *mp, UNIT *uptr) – poll for a new connection to the terminals described by mp and unit uptr.  If there is a new connection, the routine resets all the line descriptor state (including receive enable) and returns the line number (index to line descriptor) for the new connection.  If there isn’t a new connection, the routine returns –1.

void tmxr_reset_ln (TMLN *lp) – reset the line described by lp.  The connection is closed and all line descriptor state is reset.

int32 tmxr_getc_ln (TMLN *lp) – return the next available character from the line described by lp.  If a character is available, the return variable is:

(1 << TMXR_V_VALID) |  character

If no character is available, the return variable is 0.

void tmxr_poll_rx (TMXR *mp) – poll for input available on the terminals described by mp.

void tmxr_rqln (TMLN *lp) – return the number of characters in the receive queue of the line described by lp.

void tmxr_putc_ln (TMLN *lp, int32 chr) – output character chr to the line described by lp.

void tmxr_poll_tx (TMXR *mp) – poll for output complete on the terminals described by mp.

void tmxr_tqln (TMLN *lp) – return the number of characters in the transmit queue of the line described by lp.

t_stat tmxr_attach (TMXR *mp, UNIT *uptr, char *cptr) – attach the port contained in character string cptr to the terminals described by mp and unit uptr.

t_stat tmxr_detach (TMXR *mp, UNIT *uptr) – detach all connections for the terminals described by mp and unit uptr.

t_stat tmxr_ex (t_value *vptr, t_addr addr, UNIT *uptr, int32 sw) – stub examine routine, needed because the extra terminals are marked as attached; always returns an error.

t_stat tmxr_dep (t_value val, t_addr addr, UNIT *uptr, int32 sw) – stub deposit routine, needed because the extra terminals are marked as detached; always returns an error.

void tmxr_msg (SOCKET sock, char *msg) – output character string msg to socket sock.

The OS-dependent socket routines should not need to be accessed by the terminal simulators.